Module HD Audio--------------------

    Module for Intel HD Audio (ICH6, ICH6M, ESB2, ICH7, ICH8, ICH9, ICH10,
        PCH, SCH),
        ATI SB450, SB600, R600, RS600, RS690, RS780, RV610, RV620,
        RV630, RV635, RV670, RV770,
        VIA VT8251/VT8237A,
        SIS966, ULI M5461

    [Multiple options for each card instance]
    model - force the model name
    position_fix - Fix DMA pointer (0 = auto, 1 = use LPIB, 2 = POSBUF)
    probe_mask - Bitmask to probe codecs (default = -1, meaning all slots)
        When the bit 8 (0x100) is set, the lower 8 bits are used
        as the "fixed" codec slots; i.e. the driver probes the
        slots regardless what hardware reports back
    probe_only - Only probing and no codec initialization (default=off);
        Useful to check the initial codec status for debugging
    bdl_pos_adj - Specifies the DMA IRQ timing delay in samples.
        Passing -1 will make the driver to choose the appropriate
        value based on the controller chip.
    : patch - Specifies the early "patch" files to modify the HD-audio
        setup before initializing the codecs. This option is
        available only when CONFIG_SND_HDA_PATCH_LOADER=y is set.
        See HD-Audio.txt for details.
    beep_mode - Selects the beep registration mode (0=off, 1=on, 2=
        dynamic registration via mute switch on/off); the default
        value is set via CONFIG_SND_HDA_INPUT_BEEP_MODE kconfig.

    [Single (global) options]
    single_cmd - Use single immediate commands to communicate with
        codecs (for debugging only)
    enable_msi - Enable Message Signaled Interrupt (MSI) (default = off)
    power_save - Automatic power-saving timeout (in second, 0 =
        disable)
    power_save_controller - Reset HD-audio controller in power-saving mode
        (default = on)
    align_buffer_size - Force rounding of buffer/period sizes to multiples
        of 128 bytes. This is more efficient in terms of memory
        access but isn't required by the HDA spec and prevents
        users from specifying exact period/buffer sizes.
        (default = on)
    snoop - Enable/disable snooping (default = on)

    This module supports multiple cards and autoprobe.

    See Documentation/sound/alsa/HD-Audio.txt for more details about
    HD-audio driver.

    Each codec may have a model table for different configurations.
    If your machine isn't listed there, the default (usually minimal)
    configuration is set up. You can pass "model=<name>" option to
    specify a certain model in such a case. There are different
    models depending on the codec chip. The list of available models
    is found in HD-Audio-Models.txt

    The model name "genric" is treated as a special case. When this
    model is given, the driver uses the generic codec parser without
    "codec-patch". It's sometimes good for testing and debugging.

    If the default configuration doesn't work and one of the above
    matches with your device, report it together with alsa-info.sh
    output (with --no-upload option) to kernel bugzilla or alsa-devel
    ML (see the section "Links and Addresses").
       power_save and power_save_controller options are for power-saving
    mode. See powersave.txt for details.

    Note 2: If you get click noises on output, try the module option
        position_fix=1 or 2. position_fix=1 will use the SD_LPIB
        register value without FIFO size correction as the current
        DMA pointer. position_fix=2 will make the driver to use
        the position buffer instead of reading SD_LPIB register.
        (Usually SD_LPIB register is more accurate than the
        position buffer.)

    NB: If you get many "azx_get_response timeout" messages at
    loading, it's likely a problem of interrupts (e.g. ACPI irq
    routing). Try to boot with options like "pci=noacpi". Also, you
    can try "single_cmd=1" module option. This will switch the
    communication method between HDA controller and codecs to the
    single immediate commands instead of CORB/RIRB. Basically, the
    single command mode is provided only for BIOS, and you won't get
    unsolicited events, too. But, at least, this works independently
    from the irq. Remember this is a last resort, and should be
    avoided as much as possible...
: MORE NOTES ON "azx_get_response timeout" PROBLEMS:
    On some hardwares, you may need to add a proper probe_mask option
    to avoid the "azx_get_response timeout" problem above, instead.
    This occurs when the access to non-existing or non-working codec slot
    (likely a modem one) causes a stall of the communication via HD-audio
    bus. You can see which codec slots are probed by enabling
    CONFIG_SND_DEBUG_VERBOSE, or simply from the file name of the codec
    proc files. Then limit the slots to probe by probe_mask option.
    For example, probe_mask=1 means to probe only the first slot, and
    probe_mask=4 means only the third slot.

    The power-management is supported.